ANALYTICAL CHEMICAL TESTING

LABORATORY, INC.

Consulting Chemists, Scientists, & Engineers

August 22, 2013

Report To:  	Ms. Sonia Grant

564 South Ashley Street

Ann Arbor, MI 48103

Report Of:	Chemical Analysis- Water Column, Tar Ball, & Control Samples

Kalamazoo River Spill-Marshall, MI

Job #:		13-3273

Attention:	Ms. Sonia Grant                          email: Sonia.ap.grant@gmail.com

_______________________________________________________________________________

Analytical Chemical Laboratory has completed the analysis of samples received from the Kalamazoo River Spill near Marshall, Michigan.  The samples were analyzed for specific parameters, as directed and the following is reported:

Sampled:    07/26/13 by Sonia Grant, Craig Ritter

Analyzed:   07/29/13-08/07/13 by L. Butler, JSI

Reviewed:  08/22/13 by R. Naman

SAMPLE				    	 	    	                                                  IDENTIFICATION			PARAMETERS		RESULTS

ACT ID# 13-3273-0727-1                 Oil & Grease             		  <1 mg/Kg

Water Column Sample

Kalamazoo River Spill

Sampled  07-26-13 @1000

Analyzed 07-29-13 @1030

EPA 8270D  POLY-NULCLEATED AROMATIC HYDROCARBONS

SAMPLE				    	 	    	                                                 DETECTION IDENTIFICATION			PARAMETERS		RESULTS	     LIMITS

ACT ID# 13-3273-0727-2                Acenaphthylene                	    N.D.                1.27 ug/L

Water Column Sample                        Acenaphthene                	    N.D.                1.27 ug/L

Kalamazoo River Spill		            Anthracene     		           	    N.D.                1.27 ug/L

Sampled  07-26-13 @1000 	            Benzo-(a)-Anthracene 	           	    N.D.                0.25 ug/L

Analyzed 07-31-13 @1003                 Benzo-(a)-Pyrene 	           	    N.D.                1.27 ug/L

LAB# 1307239-001A			Benzo-(b)-Fluoranthene	    N.D.                0.63 ug/L						Benzo-(ghi) perylene 	           	    N.D.                1.27 ug/L

Benzo-(k)-Fluoranthene	    N.D.                0.63 ug/L

Chrysene	 	           	    N.D.                1.27 ug/L

Dibenzo-(a,h)-Anthracene       	    N.D.                0.38 ug/L

Fluorene	    		    N.D.                1.27 ug/L

Fluoranthene		           	    N.D.                1.27 ug/L

Indeno-(1,2,3 cd)-Pyrene            N.D.                0.38 ug/L

Naphthalene	                	    N.D.                1.27 ug/L

Phenanthrene  		           	    N.D.                1.27 ug/L

Pyrene		 	           	    N.D.                1.27 ug/L

2-Methylnaphthalene 	    	    N.D.                1.27 ug/L

QA/QC               PARAMETER                      % RECOVERY

2-Fluorobiphenyl                          44.1%

Terphenyl-d14                              63.6%

Nitrobenzene-d5                           38.0%

TENTATIVELY IDENTIFIED COMPOUNDS

1-MethylEthyl Benzene    	  1.43 ug/L           1.27 ug/L

1-Octadecene	      	     	  2.73 ug/L           1.27 ug/L

2-Bromoquinoxaline		  1.27 ug/L           1.27 ug/L

2-Cyclohexen-1-ol              	  74.9 ug/L           1.27 ug/L

2-Cyclohexen-1-one	           	  58.7 ug/L           1.27 ug/L

3-Chloro-cyclohexen           	  1.98 ug/L           1.27 ug/L

Bis(2-Ethylhexyl)-Hexanedioic acid  107 ug/L           1.27 ug/L

Cyclotetradecane 	           	  1.41 ug/L           1.27 ug/L

Hexadecane                    	  1.28 ug/L           1.27 ug/L

COMPARISON WITH KALAMAZOO RIVER

CONTROL SAMPLE CHROMATOGRAM

The compared sample is a fingerprint  MATCH

SAMPLE				    	 	    	                                                  IDENTIFICATION			PARAMETERS		RESULTS

ACT ID# 13-3273-0727-3                Total Petroleum           		  56 mg/Kg

Tar Ball Sample 	                         Hydrocarbons

Kalamazoo River Spill

Sampled  07-26-13 @1000

Analyzed 07-29-13 @0940

EPA 8270D  POLY-NULCLEATED AROMATIC HYDROCARBONS

SAMPLE				    	 	    	                                                DETECTION IDENTIFICATION			PARAMETERS		RESULTS           LIMITS

ACT ID# 13-3273-0727-4                Acenaphthylene                	    N.D.                145 ug/Kg Dry

Tar Ball Sample	                        Acenaphthene                	    N.D.               145 ug/Kg-Dry

Kalamazoo River Spill		            Anthracene     		           	    N.D.               145 ug/Kg-Dry Sampled  07-26-13 @1000 	            Benzo-(a)-Anthracene 	           	    N.D.               145 ug/Kg-Dry

Analyzed 08-07-13 @1313                 Benzo-(a)-Pyrene 	           	    N.D.             14.5 ug/Kg-Dry

LAB# 1307239-002A			Benzo-(b)-Fluoranthene	    N.D.              14.5 ug/Kg-Dry 					Benzo-(ghi) perylene 	           	    N.D.              14.5 ug/Kg-Dry

Benzo-(k)-Fluoranthene	    N.D.              145 ug/Kg-Dry

Chrysene	 	           	    N.D.               145 ug/Kg-Dry

Dibenzo-(a,h)-Anthracene       	   N.D.               14.5 ug/Kg-Dry

Fluoranthene	    		    N.D.          	  145 ug/Kg-Dry

Fluoranthene		           	    N.D.              145 ug/Kg-Dry

Indeno-(1,2,3 cd)-Pyrene            N.D.             14.5 ug/Kg-Dry

Naphthalene	                	    N.D.               145 ug/Kg-Dry

Phenanthrene  		           	    N.D.               145 ug/Kg-Dry

Pyrene		 	           	    N.D.               145 ug/Kg-Dry

2-Methylnaphthalene 	    	    N.D.               145 ug/Kg-Dry

QA/QC               PARAMETER                      % RECOVERY

2-Fluorobiphenyl                          30.2%

Terphenyl-d14                              39.5%

Nitrobenzene-d5                           43.8%

TENTATIVELY IDENTIFIED COMPOUNDS

1-MethylEthyl Benzene             292 ug/Kg    145 ug/Kg-Dry                                                                2-Cyclohexen-1-ol                   	 2,510 ug/Kg   145 ug/Kg-Dry                               			2-Cyclohexen-1-one	              1,340 ug/Kg     145 ug/Kg-Dry
\

COMPARISON WITH KALAMAZOO RIVER

CONTROL SAMPLE CHROMATOGRAM

The compared sample is a fingerprint  MATCH

EPA 8270D  POLY-NULCLEATED AROMATIC HYDROCARBONS

SAMPLE				    	 	    	                                                DETECTION IDENTIFICATION			  PARAMETERS		RESULTS          LIMITS

ACT ID# 13-3273-0727-5                   Acenaphthylene                	    N.D.                30 mg/Kg

CONTROL-Spilled Oil Sample/Paper  Acenaphthene                	    N.D.                30 mg/Kg

Kalamazoo River Spill		              Anthracene     		    N.D.                30 mg/Kg

Sampled  07-26-13 @1000 	              Benzo-(a)-Anthracene 	    N.D.                30 mg/Kg

Analyzed 08-07-13 @1430                   Benzo-(a)-Pyrene 	         	    N.D.               0.3 mg/Kg

LAB# 1307239-003A			  Benzo-(b)-Fluoranthene	    N.D.               0.3 mg/Kg						  Benzo-(ghi) perylene 	           	    N.D.                30 mg/Kg

Benzo-(k)-Fluoranthene	    N.D.                30 mg/Kg

Chrysene	 	           	    N.D.                30 mg/Kg

Dibenzo-(a,h)-Anthracene         N.D.               0. 3 mg/Kg

Fluoranthene	    		    N.D.         	    30 mg/Kg

Fluoranthene		           	    N.D.                30 mg/Kg

Indeno-(1,2,3 cd)-Pyrene          N.D.               0.3 mg/Kg

Naphthalene	                	    N.D.               145 ug/Kg

Phenanthrene  		    N.D.               145 ug/Kg

Pyrene		 	           	    N.D.               145 ug/Kg

2-Methylnaphthalene 	    	    N.D.               145 ug/Kg

QA/QC               PARAMETER                      % RECOVERY

2-Fluorobiphenyl                          42.3%

Terphenyl-d14                              48.6%

Nitrobenzene-d5                           34.5%

TENTATIVELY IDENTIFIED COMPOUNDS

Eicosane	 		    286 mg/Kg 	    30 mg/Kg

Heptadecane			    223 mg/Kg  	    30 mg/Kg

Pentacosane                                 287 mg/Kg  	    30 mg/Kg

Tetradecane    		    	    227 mg/Kg  	    30 mg/Kg

Tetracosane 	  		    275 mg/Kg  	    30 mg/Kg

TIC COMPOUND AND CHROMATOGRAM REVIEW AND COMPARISON TO THE KALAMAZOO RIVER OIL SPILL OF 2010 NEAR MARSHALL MICHIGAN

ACT Laboratory Chemist, Mr. Robert M. Naman has reviewed sample data from water columns and tar ball samples tested from the Kalamazoo Oil Spill of 2010.  ACT has compared this data with that of a Control sample that was provided and extracted from a piece of paper dipped into the actual oil spill.  PAH constituents were analyzed for and no detection of the listed compounds in the method used resulted from the analysis.  Tentatively Identified Compounds were also reported for each PAH analysis and the data was reviewed.  Chromatograms were closely scrutinized using a light table and compounds present in each sample were compared.  Retention times and relative quantities were assessed.

Based on our review ACT Laboratory Senior Scientist Mr. Robert M. Naman is pleased to offer the following professional intellectual opinion.  ACT opines that the source of the Water Column Components and the Tar Ball Components is generally scientifically traceable from chromatogram data and shows that the control sample very likely produced the compounds found in the water column samples and in the Tar ball samples. After review, discussion of the data and the chromatograms with Mr. Dave Kahler of Geolabs, Inc. of Braintree MA, the Lab that performed the 8270D PAH Analyses on the samples and Mr. Kahler concurs with the opinions of ACT Laboratory Senior Chemist Mr. Robert M. Naman.  Mr. Kahler will also provide a discussion of his review and opinion under separate cover.  His review will be electronically sent to you when it is received by ACT Laboratory, Inc., which should be late today or early tomorrow, August 23, 2013.

TIC COMPOUND AND CHROMATOGRAM REVIEW AND COMPARISON OF KALAMAZOO RIVER OIL SPILL OF 2010  TO MACONDO 252 BRITISH PETROLEUM GULF OF MEXICO OIL SPILL of 2010 WITH REGARDS TO  SURFACTANT USE

ACT also took the opportunity to review previous data from archived samples that show the resultant compounds from the mixture of Corexit 9527, Corexit 9727A, and Corexit 9500--all surfactants used in the BP Gulf Oil Spill of 2010, and Macondo 252 Crude Oil.  The TIC compounds present in the water column and in the tar balls recently analyzed from the Kalamazoo River Spill of 2010, showed resulting compounds that are clearly identical to the TIC compounds produced from mixing Corexit compounds with crude oil, as in the BP Oil spill of 2010 in the Gulf of Mexico.  It is blatantly clear that surfactants were used as well in the Kalamazoo River Spill of 2010 and the resulting compounds present mimic those formed and still present in the areas affected by the BP oil spill of 2010.

We appreciate this opportunity to be of service.  If there are any questions, please feel free to call.

Very truly yours,

ANALYTICAL CHEMICAL TESTING LABORATORY, INC.

Robert M. Naman, President

Analytical Chemist

E-Mail:  robertnaman@aol.com

Fellow, American Institute

of Chemists, Reg. 15488

RMN/lcb

Attachments:  Sonia Grant Job Documents